## Slide 1
Computer Architecture
The Fundamental
Course Number : TTH2D3
CLO : 1
Week : 1
CLO#1 Student have the knowledge to explain microprocessor system
[C2] Understand the history of microprocessor and microcontroller
[C2] Understand the architecture of computer system
[C2] Understand the design of minimum system for microcontroller

## Slide 2
Why do we need to take this course?

## Slide 3: IoT Growth Rate
Source: Forbes

## Slide 4: Heat Map of IoT by Industry and Application
Source: Forbes

## Slide 5
Why do we need to take this course?
Because everything will be connected through The Internet, and it starts with what you will learn in this course, i.e. microcontroller.

## Slide 6: What is Organization and how it differ with Architecture?
Computer Organization
describes each unit’s functionality, like input, storage, process, and output.
Computer Architecture
describes the interconnection between units and how they work together, including hardware and software.

## Slide 7: Computer System Hardware

## Slide 8: Microprocessor
The Fundamental

## Slide 9: Microprocessor: Historical Review (1/3)
Intel 4004 (1969)
Intel 8008 (1972)
2300 transistor
29000 transistor
29000 transistor
Intel 8088 (1981)
Intel 286 (1982)
134000 transistor
Intel 386 (1985)
275000
transistor
Intel 486 (1989)
1,2 million transistor

## Slide 10: Microprocessor: Historical Review (2/3)
Intel 586 (1993)
Intel P-II (1997)
Intel P4 (2000)
Intel P-III (1999)
Intel Pentium-M (2003)
Intel Pentium-D (2005)
Intel Itanium (2006)

## Slide 11: Microprocessor: Historical Review (3/3)

## Slide 12: Microprocessor Complexity
Intel 4004 with 2300 transistors (1969)
Intel Itanium with 330 million transistors (2005)

## Slide 13: Microprocessor Complexity (in Detail)
Microprocessor Type | Year | Speed | Word | Transistors | MIPS
4004 | 1969 | 108 kHz | 4 bit | 2300 | 0.06
8008 | 1972 | 200 kHz | 8 bit | 3500 | 0.06
8080 | 1974 | 2 MHz | 8 bit | 6000 | 0.64
8086 | 1978 | 4.47 MHz | 16 bit | 29000 | 0.66
8088 | 1981 | 4.47 MHz | 16 bit | 29000 | 0.75
80286 | 1982 | 12 MHz | 16 bit | 134000 | 2.66
80386 | 1985 | 16-33 MHz | 32 bit | 275000 | 4
80486 (i486) | 1989 | 20-100 MHz | 32 bit | 1.2 million | 70
80586 (Pentium) | 1993 | 75-200 MHz | 32 bit | 3.3 million | 126-203
Pentium Pro | 1995 | 150-200 MHz | 32 bit | 5.5 million | 300
Pentium MMX | 1997 | 166-233 MHz | 32 bit | 4.5 million | 
Pentium II | 1997 | 233-450 MHz | 32 bit | 7.5 million | 
Pentium III | 1999 | 450-933 MHz | 32 bit | 9.5 million | 
Itanium | 2000 | 1 GHz | 64 bit | 15 million | 1200

## Slide 14: Intel i7

## Slide 15: Definition
Microprocessor is a:
LSI/VLSI (Very Large Scale Integration), designed to process information, any information.
Multipurpose or General Purpose LSI/VLSI
Sometimes (incorrectly) named CPU (Central Processing Unit)
Fabricated on a die chip

## Slide 16: Definition
Microprocessor System is a:
System consists of at least 1 microprocessor and a support system
Support system may include:
  Memory unit
  Input unit
  Output unit

## Slide 17: Computer System Architecture
uP
Input
#1
uP
Output
#2
uP
Input
#3
Output
uP
Input
#4
uP
Output
#5
uP
Input
#6
Output
Memory
Memory
Memory

## Slide 18: Support System
Memory
  Static RAM, Dynamic RAM, ROM, EPROM, Flash Disk, Hard Disk
Input
  Keyboard, Mouse, Touch Pad, Scanner, ADC
Output
  Monitor, Speaker, VR, Printer, DAC

## Slide 19: Inside the Microprocessor
ALU
Register
Control Unit
Bus

## Slide 20: Inside the Microprocessor
ALU, Arithmetic and Logic Unit responsible for calculation
Register, a special type (very fast) of memory responsible for storing instruction, data, address, and status
Control Unit responsible to control the works
Bus responsible for transferring signal (control, data, address)

## Slide 21: How it Works?
C = A + B
ALU
CU
A
B
C
Data Register
ADD A,B  C
Instruction Register
2
2
1
3

## Slide 22: Microprocessor: Basic functionalities
Able to locate where the instruction and data resides
Able to fetch the instruction and data from memory
Able to store instruction and data in register
Able to decode and understand the instruction
Able to execute the instruction
Able to manage all process in a proper sequence

## Slide 23: Memory
Why do we need memory? to store data and instruction
What is memory hierarchy? a hierarchy of memory types
What are memory types? internal vs. external, accessibility, media
data
data
data
data
address 1
address 2
address 3
address 4

## Slide 24: Hierarchy Memory
is a way to balance capacity, speed, and price
Secondary Memory
(Hard Disk)
Main Memory
(DRAM)
Cache
(SRAM)
Register
BIGGER CAPACITY
FASTER SPEED
HIGHER PRICE

## Slide 25: Memory Types
Internal vs. External
  Register, RAM, Hard Disk, CD/DVD
Accessibility
  ROM (Read Only Memory), PROM (Programmable ROM), EPROM (Erasable PROM), EEPROM (Electrically EPROM)
  RAM (Random Access Memory), SRAM (Static RAM), DRAM (Dynamic RAM)
Media
  Electric charge, Optic, Magnetic

## Slide 26: Interaction between Microprocessor and Memory
There are 2 types of interaction:
READ operation (retrieve), where microprocessor retrieves data from memory
WRITE operation (store), where microprocessor stores data into memory

## Slide 27: How Microprocessor READs from Memory?
Microprocessor prepares and outputs the address of data that need to be retrieved for processing
Microprocessor sends a READ signal to memory
After receiving a READ signal, memory locate the data based on given address
Memory provides the data into data bus

## Slide 28: How Microprocessor WRITEs into Memory?
Microprocessor prepares and outputs the address of data that need to be stored in memory
Microprocessor provides data into data bus
Microprocessor sends a WRITE signal to memory
After receiving a WRITE signal, memory read the data bus and stores the data using given address

## Slide 29: Machine Instruction
The Fundamental

## Slide 30: Machine Instruction Type
Data Transfer, ex: MOV, PUSH, POP
Arithmetic and Logic, ex: ADD, SUB, AND, OR, SHL
Control, ex: JMP, JZ

## Slide 31: How Microprocessor RUNS an instruction?
Instruction Fetch (IF) is where microprocessor fetch the instruction from memory
Instruction Decode (DE) is where the microprocessor decode the instruction to understand what needs to be done
Execution (EX) is where te microprocessor execute the instruction
Instruction Fetch
Instruction Decode
Execution

## Slide 32: Input and Output
Is an interface unit to communicate with outside the system’s world
Input unit receives data and in many cases also transforms signal from outside world (example, ADC Analog to Digital Converter)
Output unit delivers data and in many cases also transforms the data into specific signal (example, DAC Digital to Analog Converter)

## Slide 33: Clock
Clock: is a digital periodic and independent signal, delivered to all units for synchronization
Clock is generated using crystal oscillator with specific frequency

## Slide 34: Bus System
There are 3 types of bus:
Data bus
Address bus
Control bus

## Slide 35: Microcontroller
The Fundamental

## Slide 36: What is the difference between Microprocessor and Microcontroller?
Microcontroller is a single chip CPU that already consists of:
  Processor (ALU + Unit Control)
  Internal Memory RAM
  Input / Output
  Timer
  Interrupt Control
Microcontroller is designed for a specific purpose, which makes it only applicable for 1 domain

## Slide 37: Microcontroller

## Slide 38: Atmel Microcontroller
To be fully functional, a microcontroller needs:
Power suply
Clock generator
Power Reset

## Slide 39: AT89CXX
AT89C
Data Bus
Address Bus
Control Bus
Data Bus
Address Bus
Control Bus
+5 V
Gound
Data Bus (8 bit) for transferring data from or to AT89CXX
Address Bus (16 bit) for:
  indicating the address of data in memory
  indicating which I/O that want to be connected
Control Bus for delivering signal to other peripherals, such as memory and I/O

## Slide 40: See you on next class