## Slide 1
Microcontroller
Minimum System
Course Number : TTH2D3
CLO : 1
Week : 5-7
CLO#1 Student have the knowledge to explain microprocessor system
[C2] Understand the history of microprocessor and microcontroller
[C2] Understand the architecture of computer system
[C2] Understand the design of minimum system for microcontroller

## Slide 2: How it Works?
C = A + B
ALU
CU
A
B
C
Data Register
ADD A,B  C
Instruction Register
2
2
1
3

## Slide 3: What is the difference between Microprocessor and Microcontroller?
Microcontroller is a single chip CPU that already consists of:
  Processor (ALU + Unit Control)
  Internal Memory RAM
  Input / Output
  Timer
  Interrupt Control
Microcontroller is designed for a specific purpose, which makes it only applicable for 1 domain

## Slide 4: Atmel Microcontroller
To be fully functional, a microcontroller needs:
Power suply
Clock generator
Power Reset

## Slide 5: AT89CXX
AT 89CXX
Data Bus
Address Bus
Control Bus
+5 V
Ground
Data Bus (8 bit) for transferring data from or to AT89CXX
Address Bus (16 bit) for:
  indicating the address of data in memory
  indicating which I/O that want to be connected
Control Bus for delivering signal to other peripherals, such as memory and I/O

## Slide 6: Microcontroller
Minimum System

## Slide 7: AVR Microcontroller
Designed and fabricated by Atmel
Simple, low-cost, high-performance and full features

## Slide 8: References 1
Flash is a ROM, used for storing user-defined program that need to be run by the microcontroller
RAM (Random Acces Memory), used for storing data temporarily while program runs
EEPROM (Electrically Erasable Programmable Read Only Memory), used for store data permanently (as a result of a program)
I/O port, is a pin for communication purposes with other devices

## Slide 9: References 2
Timer is a hardware module to count time (pulse)
UART (Universal Asynchronous Receive Transmit), used for asynchronous data communication
PWM (Pulse Width Modulation), used for creating pulse modulation
ADC (Analog to Digital Converter), used for converting analog signal into digital representation

## Slide 10: References 3
SPI (Serial Peripheral Interface), used for synchronous serial data communication
ISP (In System Programming), used for direct programming into the system

## Slide 11: About ATMega 8535
ATMega8535 is a 8-bit CMOS RISC architecture
Most instruction are executed in 1 clock cycle, which makes a 1 MIPS per MHz
4 I/O programmable port for many applications

## Slide 12: ATMega 8535 Architecture
4 I/O port (4x8) Port A, B, C and D
ADC (Analog to Digital Converter)
3 Timer/Counter
32 register
512 byte SRAM
8kb Flash memory
Internal and external interrupt
SPI interface port to download program into flash
512 byte EEPROM
Analog comparator interface
USART port for serial communication

## Slide 13: See you on next class

## Slide 14: ATMega 8535: Memory Map
Flash stores user-defined program
RAM stores temporary data
EEPROM stores permanent data

## Slide 15: ATMega 8535: Memory Map
Flash memory (non-volatile) has 4k word (1 word = 2 byte) 0x000 - 0xFFF
Use Program counter (PC) to address flash

## Slide 16: ATMega 8535: Memory Map
Static RAM (volatile):
32 general purpose register (0x00 - 0x1F)
64 I/O register (0x20 - 0x5F)  control C peripheral functionality
SRAM internal (0x60 - 0x25F)

## Slide 17: MICROCONTROLLER (C) AVR ATMEGA 8535

## Slide 18: C ATMega 8535: Features
C AVR ATMega 8535 has 40 pins where 32 pins used for parallel port.
Each parallel port has 8 pins, so C AVR ATMega 8535 has 4 parallel ports, port A, B, C, and D.
Each pin in parallel port has designated name, like portA.0 to portD.7

## Slide 19: PORT A
Pin 33 to 40 are for parallel port A (8 bit directional I/O)
Each pin has internal pull-up resistor to provide electric current up to 20 mA to charge LED display directly
To enable port A we have to set Data Direction Register port A (DDRA). Bit DDRA = 0 means that specific pin become input (1 for output)
Special functionality: each pin in port A can also be used for analog input (ADC)

## Slide 20: PORT B
Pin 1 to 8 are for parallel port B (8 bit directional I/O)
Each pin has internal pull-up resistor to provide electric current up to 20 mA to charge LED display directly
To enable port B we have to set Data Direction Register port B (DDRB). Bit DDRB = 0 means that specific pin become input (1 for output)
Port Pin | Special Functionality
PB0 | T0 = timer/counter 0 external counter input
PB1 | T1 = timer/counter 0 external counter input
PB2 | AIN0 = analog comparator positive input
PB3 | AIN1 = analog comparator negative input
PB4 | SS = SPI slave select input
PB5 | MOSI = SPI bus master output / slave input
PB6 | MISO = SPI bus master input / slave output
PB7 | SCK = SPI bus serial clock

## Slide 21: PORT C
Pin 22 to 29 are for parallel port C (either input or output)
Each pin has internal pull-up resistor to provide electric current up to 20 mA to charge LED display directly
To enable port C we have to set Data Direction Register port C (DDRC). Bit DDRC = 0 means that specific pin become input (1 for output)
Pin | Special Functionality
PC.7 | TOSC2 (Timer Oscillator Pin 2)
PC.6 | TOSC1 (Timer Oscillator Pin 1)
PC.1 | SDA (Two-Wire Serial Bus Data Input/Output Line)
PC.0 | SCL (Two-Wire Serial Bus Clock Line)

## Slide 22: PORT D
Pin 14 to 20 are for parallel port D (8 bit directional I/O)
Each pin has internal pull-up resistor to provide electric current up to 20 mA to charge LED display directly
To enable port D we have to set Data Direction Register port D (DDRD). Bit DDRD = 0 means that specific pin become input (1 for output)
Port Pin | Special Functionality
PD0 | RDX (UART input line)
PD1 | TDX (UART output line)
PD2 | INT0 ( external interrupt 0 input )
PD3 | INT1 ( external interrupt 1 input )
PD4 | OC1B (Timer/Counter1 output compareB match output)
PD5 | OC1A (Timer/Counter1 output compareA match output)
PD6 | ICP (Timer/Counter1 input capture pin)
PD7 | OC2 (Timer/Counter2 output compare match output)

## Slide 23: Other Pins
RESET RST on pin 9 is a reset for AVR, activated with low voltage in at least 2 machine cycle XTAL1 and XTAL2 XTAL1 on pin 13 and XTAL2 on pin 12 is an input for oscillator crystal AVcc AVcc on pin 10 is an input for ADC externally connected to Vcc via LPF AREF AREF on pin 32 is a reference input voltage for ADC

## Slide 24: ATMega 8535: Minimum System
Minimum System of a C is the most simplest circuit to make it works

## Slide 25: ATMega 8535: Minimum System: Power Supply
Most C use +5 VDC for power supply, it could be either uses 3x1,5VDC batteries or 220VAC power outlet
7805 is a +5VDC power regulator

## Slide 26: ATMega 8535: Minimum System: Oscillator
Oscillator = pulse generator
C ATMega 8535 has an internal 8 MHz oscillator, but sometimes we need faster or slower system
C ATMega 8535 can works as fast as 16 Mhz

## Slide 27: ATMega 8535: Minimum System: ISP
ISP = In-System Programming
C ATMega 8535 can be programmed via parallel or serial

## Slide 28: ATMega 8535: Minimum System: Reset
Reset button
Similar with reset button in PC/laptop (using power button)
When reset is activated, C will restart from the beginning

## Slide 29: See you on next class