## Slide 1
Programming Microcontroller
Assembly and C
Course Number : TTH2D3
CLO : 2
Week : 5-7
CLO#2 Student have the knowledge to create basic programming for microcontroller
[C3] Understand how to program in Assembly
[C3] Understand how to program a microcontroller using C
[C3] Understand how to store the program in microcontroller

## Slide 2: What is the difference between P, C, and Development Board?
development board
microcontroller
microprocessor
CU
Register
ALU
memory
Flash
SRAM
EEPROM
Programmable
Input / Output
Programmable
Interrupt Controller
Programmable
Timer / Counter
External Memory
Power
Regulator
(Crystal) Clock
Regulator
Pin Connector

## Slide 3: MICROCONTROLLER (C) AVR ATMEGA 8535

## Slide 4: ATMega 8535 Architecture
4 I/O port (4x8) Port A, B, C and D
ADC (Analog to Digital Converter)
3 Timer/Counter
32 register
512 byte SRAM
8kb Flash memory
Internal and external interrupt
SPI interface port to download program into flash
512 byte EEPROM
Analog comparator interface
USART port for serial communication

## Slide 5: Prerequisite for Programming a Microcontroller
Before you start to program a C, you need to understand 2 things:
  The Instruction Set of the C
  The hardware capability of the C
Most C comes with an IDE (Integrated Development Environment) to build and run your program
For Atmel C, you may choose either Assembly or C for your programming language

## Slide 6: Instruction Set
ATMega 32

## Slide 7: What is Instruction Set?
Instruction is like a command to be executed by Control Unit within the P
Instruction is usually grouped by 4 types:
  Data transfer (ex. MOV)
  Arithmetic and Logic (ex. ADD)
  Control Transfer (ex. JMP)
  Miscellaneous (ex. NOP)
Every P has their own instruction
Instruction set is the list of instruction understood only by a specific P

## Slide 8: Basic Instruction (1/2)
LDI (Load Immediate): writes a constant into a register ex. LDI R16,0xFF (writes FFH into register 16)
OUT: writes data from register to a specific I/O port ex. OUT DDRA,R16 (writes data from register 16 to port A)
IN: reads data from a specific I/O port into a register ex. IN R16, PORTA (reads data from port A and stores it to register 16)
SBI (Set bit in I/O): set (put into High Voltage) a bit in I/O port ex. SBI PORTA,0 (set bit 0 in port A to High Voltage)
CBI (Clear bit in I/O): unset (put into Low Voltage) a bit in I/O port ex. CBI PORTA,1 (set bit 1 in port A to Low Voltage)

## Slide 9: Basic Instruction 2/2
SBIS (Skip if bit in I/O is set): skip 1 instruction below if a specific bit in I/O port is set (High Voltage) ex. SBIS PORTA,2 RJMP RPT “RJMP RPT” will be skipped if bit 2 in port A is High Voltage
SBIC (Skip if bit in I/O is cleared): skip 1 instruction below if a specific bit in I/O port is unset (Low Voltage) ex. SBIC PORTA,2 RJMP RPT “RJMP RPT” will be skipped if bit 2 in port A is Low Voltage

## Slide 10: Arithmetic Instruction (1/4)

## Slide 11: Arithmetic Instruction (2/4)

## Slide 12: Arithmetic Instruction (3/4)

## Slide 13: Arithmetic Instruction (4/4)

## Slide 14: Branch Instruction (1/4)

## Slide 15: Branch Instruction (2/4)

## Slide 16: Branch Instruction (3/4)

## Slide 17: Branch Instruction (4/4)

## Slide 18: Data Transfer Instruction (1/4)

## Slide 19: Data Transfer Instruction (2/4)

## Slide 20: Data Transfer Instruction (3/4)

## Slide 21: Data Transfer Instruction (4/4)

## Slide 22: Bit Test Instruction

## Slide 23: Control Instruction

## Slide 24: Assembly Example

## Slide 25: Hardware Capability

## Slide 26: ATMega 32: Pin Layout
Port A
Port B
Port D
Port C

## Slide 27: ATMega32 Pin out & Descriptions

## Slide 28: Port Description

## Slide 29: ATMega32 Pin out & Descriptions

## Slide 30: Single pin accessing

## Slide 31: Example

## Slide 32: Using C Language to Program your Microcontroller

## Slide 33: An Example of ATMEL Program in C Language

## Slide 34: Comment
Ignored by compiler but very useful for other to understand the program
  /* for writing comment in a paragraf */
  // for writing a 1 line comment

## Slide 35: Preprocessor (6-10)
Preprocessor #include can be used to attach a library function (h header file) so we may use many built in functions
Header “io.h” contains definition for SFR (Special Function Register) and all pins and bits in C
Preprocessor #define is used for defining a constant or macro

## Slide 36: Variable Declaration
Variable is used to store a value within a program
A global variable is defined outside any function and can be accessed by all functions
A local variable is defined inside a function and can only be accessed by that function
How to define variable:
  DataType VariableName;

## Slide 37: Function Prototype
Used to define a function to be called by other function (usually by main function)
How to define function:
  DataType FunctionName (DataType Parameter1, DataType Parameter 2)

## Slide 38: Main Function
The first function to be executed starting from the first line
How to call a function from main function:
  Without return value and without input parameter function()
  With return value but without input parameter variable = functionName();
  With return value and with input parameter variable = functionName(variable_or constant)

## Slide 39: Sub-Program or Function
Function is a sub module to solve a specific problem (ex. calculate factorial)
How to define a function:
  Without return value and without input parameter void function(void)
  With return value but without input parameter DataType functionName(void);
  With return value and with input parameter DataType functionName(DataType parameter1, ...)

## Slide 40: Data Type
Data Type | Byte | Bit | min | Max
char | 1 | 8 | -128 | 127
signed char | 1 | 8 | -128 | 127
unsigned char | 1 | 8 | 0 | 255
Int | 2 | 16 | -32768 | 32767
signed int | 2 | 16 | -32768 | 32767
unsigned int | 2 | 16 | 0 | 65535
long | 4 | 32 | -2147483648 | 2147483647
signed long | 4 | 32 | -2147483648 | 2147483647
unsigned long | 4 | 32 | 0 | 4294967295
float | 4 | 32 | 1,28E-38 | 3,4E38

## Slide 41: ATMEL Studio
Please try to explore the ATMEL Studio using provided example projects

## Slide 42: See you on next class