## Slide 1: Antrian Prioritas
Usage Parameter Control

## Slide 2
Shaping increases network efficiency by reducing output bandwidth
without shaping
Re-space the input cells
With shaping

## Slide 3
CAC examines whether network resources are sufficient or not for a new
Time
Bit rate
CAC
Necessary bandwidth < Space of bandwidth ?
accept or reject
Already in use

## Slide 5
QoS Design
Contoh : Kualitas Voice dalam Jaringan VoIP dipengaruhi langsung oleh dua faktor utama :
Packet loss
Delay Packet
Selain itu, echo tidak langsung indirectly disebabkan kualitas voice pada jaringan VoIP

## Slide 6
Packet Delay
Packet delay can cause either voice-quality degradation, due to the end-to-end voice latency, or packet loss, if the delay is variable. If the end-to-end voice latency becomes too long (250 msec, for example
Packet Loss
There are several reasons for packet loss, including:
  1. Congestion caused by queues overflowing their packet limits
  2. Network nodes running out of buffer space
  3. Memory limitations in network nodes
  4. Policing, or controls that watch traffic flows, ensuring that they conform to certain bandwidth levels. If bandwidth levels are exceeded, policing controls will drop all packets exceeding the given rate.

## Slide 7
Echo
Echo bukan masalah khusus terhadap packet switching tetapi berpengaruh pada teknologi Circuit switching yang disebabkan oleh dua hal :
Level input sinyal (gain)/level sinyal output (attenuation)
Mismatch Impedansi.

## Slide 8
Komponen Fixed Delay
Propagation—six microseconds per kilometer
Serialization
Processing
  Coding/compression/decompression/decoding
  Packetization

## Slide 9
Komponen Variable Delay
Queuing delay
Dejitter buffers
Variable packet sizes

## Slide 10
Gateway Processing

## Slide 11
Contoh dalam VoIP QoS :
  Classification
  Queuing
  Network provisioning

## Slide 12: Queuing’s Premise
Getting better service is a matter of managing congested queues
Over-all latency and bandwidth are constant
  Make some traffic absorb latency, and therefore give up bandwidth
  Shield other traffic from latency, and therefore gain bandwidth

## Slide 13: FIFO Queuing
Premise
  “Packets leave in order of arrival”
Fixed queue lengths
  Results in dropping from tail of queue under load
  Results in flow synchronization

## Slide 14: Simplest QoS Algorithm: Priority Queuing
Stated requirement:
  “If <application> has traffic waiting, send it next”
Commonly implemented
  Defined behaviour of IP precedence

## Slide 15: Priority Queuing Implementation Approach
Identify interesting traffic
  Access lists
Place traffic in various queues
De queue in order of queue precedence

## Slide 16
Priority Queuing (PQ)
Traffic Destined for Interface
Classification by:
Protocol (IP, IPX, AppleTalk, SNA, DecNet, Bridge, etc.)
Incoming Interface (EO, SO, S1, etc.)
Interface Buffer Resources
Transmit Queue
Output Line
Interface Hardware
Ethernet
Frame Relay
ATM
Serial Link
Etc.
High
Medium
Normal
Low
Q Length Defined by Q Limit
Classify
Absolute Priority Scheduling

## Slide 17: Priority Queuing
Priority (Access) List
Forwarder
Low Priority
Medium Priority
High Priority
Transmission Queue
Classification

## Slide 18: Pitfalls of Priority Queuing
Can cause traffic lockout if not well engineered
FIFO by priority:
  Within priority, still unpredictable

## Slide 19: Class-Based Queuing
One standard : custom queuing
Stated requirement:
  “Traffic with <characteristics> needs a guaranteed rate or latency”
“Characteristics” may be:
  Application
  Traffic source

## Slide 20: Custom Queuing Implementation Approach
Identify the traffic
Distribute into FIFO queue by class
Dequeue in some rotation
  Remove some number of bytes at most
  Move to next queue in round robin order

## Slide 21
Traffic Destined for Interface
Interface Buffer Resources
Q Length Deferred by Queue Limit
Up to 16
3/10
1/10
Weighted Round Robin Scheduling
(byte count)
Classification by:
Protocol (IP, IPX, AppleTalk, SNA, DecNet, Bridge, etc.)
Incoming interface (EO, SO, S1, etc.)
Allocate Proportion of Link Bandwidth)
Classify
Interface Hardware
Ethernet
Frame Relay
ATM
Serial Link
Etc.
2/10
3/10
2/10
Link Utilization Ratio
Transmit Queue
Output Line

## Slide 22: Custom Queuing
Queue #0
Transmission Queue
Queue #1
Queue #2
Queue #3
Queue #4
Queue #5
Queue #6
Queue #9
Queue #10
Queue #11
Queue #12
Queue #13
Queue #14
Queue #15
Queue #7
Queue #16
Queue #8
Control Traffic
Priority (Access) List
Forwarder

## Slide 23: Pitfalls of Custom Queuing
FIFO by class:
  Within class, still unpredictable

## Slide 24: Weighted Fair Queuing (WFQ)
Stated requirement:
  “Traffic latency must be predictable”
  “Reserved flows must achieve a certain bandwidth and latency”

## Slide 25: Fair Queuing Approach
Enqueue traffic in the sequence the TDM would deliver it
As a result, be as fair as the TDM

## Slide 26: Effects of Fair Queuing
Low-bandwidth flows get
  As much bandwidth as they can use
  Timely service
High-bandwidth flows
  Interleave traffic
  Cooperatively share bandwidth
  Absorb latency

## Slide 27: What Weighting Does
In TDM
  Channel speed determines message “duration”
In WFQ
  Multiplier on message length changes simulated message “duration”
Result:
  Flow’s “fair” share predictably unfair

## Slide 28: Weighted Fair Queuing (WFQ)
Traffic Destined for Interface
Interface Buffer Resources
Configurable Number of Queues
Flow-Based Classification by:
Source and destination address
Protocol
Session identifier (port/socket)
Weight Determined by:
Requested QoS (IP Procedure, RSVP)
Frame Relay FECN, BECN, DE (For FR Traffic)
Flow throughput (weighted-fair)
Weighted Fair Scheduling
Classify
Transmit Queue
Output Line

## Slide 29
end